## Slide 1: SIP Session Timer Glare Handling
IETF#101
London, UK
draft-ietf-sipcore-sessiontimer-race-01
Christer.Holmberg@ericsson.com
Christer Holmberg
ER
2018-03-14

## Slide 2: THE AGENDA
THE FLOW
  Real-life deployment use-case causing problem
THE BLAME
  Different opinions on which entity to blame
THE STANDARD
  Ambiguities/missing parts in RFC 4028
THE SOLUTION
  Describing the solution currently defined in the draft
THE LIST
  Picks from the mailing list comments on the defined solution
THE WAY FORWARD

## Slide 3: THE FLOW
UA Proxy AS
------------------->
INVITE (#1)
Supported:timer
SE:refresher=uac
------------------->
INVITE (#2)
Supported:timer
SE:refresher=uac
<-------------------
18x (#3)
<-------------------
18x (#4)
+++early dialog established +++

## Slide 4: THE FLOW
UA Proxy AS
------------------->
INVITE (#1)
Supported:timer
SE:refresher=uac
------------------->
INVITE (#2)
Supported:timer
SE:refresher=uac
<-------------------
18x (#3)
<-------------------
18x (#4)
+++early dialog established +++
The 18x does not contain the SE (Session-Expires) header field, because only allowed in INVITE, UPDATE and 2xx.

## Slide 5: THE FLOW
UA Proxy AS
<-------------------
UPDATE (#5)
Supported:timer
SE:refresher=uas
<-------------------
UPDATE (#6)
Supported:timer
SE:refresher=uas
------------------->
200 (UPDATE) (#7)
------------------->
200 (UPDATE) (#8)
Require:timer
SE:refresher=uac
<-------------------
480 (INVITE) (#9)
<-------------------
480 (INVITE (#10)

## Slide 6: THE FLOW
UA Proxy AS
<-------------------
UPDATE (#5)
Supported:timer
SE:refresher=uas
<-------------------
UPDATE (#6)
Supported:timer
SE:refresher=uas
------------------->
200 (UPDATE) (#7)
------------------->
200 (UPDATE) (#8)
Require:timer
SE:refresher=uac
<-------------------
480 (INVITE) (#9)
<-------------------
480 (INVITE (#10)
When UPDATE request is sent, the initial session timer negotiation is still ongoing. Refresher role is changed from uac to uas.

## Slide 7: THE FLOW
UA Proxy AS
<-------------------
UPDATE (#5)
Supported:timer
SE:refresher=uas
<-------------------
UPDATE (#6)
Supported:timer
SE:refresher=uas
------------------->
200 (UPDATE) (#7)
------------------->
200 (UPDATE) (#8)
Require:timer
SE:refresher=uac
<-------------------
480 (INVITE) (#9)
<-------------------
480 (INVITE (#10)
When UPDATE request is sent, the initial session timer negotiation is still ongoing. Refresher role is changed from uac to uas.
"In a session refresh request sent within a dialog with an active session timer, the Session-Expires header field SHOULD be present.“
Q: Is session timer “active”?

## Slide 8: THE FLOW
UA Proxy AS
<-------------------
UPDATE (#5)
Supported:timer
SE:refresher=uas
<-------------------
UPDATE (#6)
Supported:timer
SE:refresher=uas
------------------->
200 (UPDATE) (#7)
------------------->
200 (UPDATE) (#8)
Require:timer
SE:refresher=uac
<-------------------
480 (INVITE) (#9)
<-------------------
480 (INVITE (#10)
When UPDATE request is sent, the initial session timer negotiation is still ongoing. Refresher role is changed from uac to uas.
"In a session refresh request sent within a dialog with an active session timer, the Session-Expires header field SHOULD be present.“
Q: Is session timer “active”?
The UA does not include refresher in the UPDATE response. UA considers session-timer negotiation still ongoing?

## Slide 9: THE FLOW
UA Proxy AS
<-------------------
UPDATE (#5)
Supported:timer
SE:refresher=uas
<-------------------
UPDATE (#6)
Supported:timer
SE:refresher=uas
------------------->
200 (UPDATE) (#7)
------------------->
200 (UPDATE) (#8)
Require:timer
SE:refresher=uac
<-------------------
480 (INVITE) (#9)
<-------------------
480 (INVITE (#10)
When UPDATE request is sent, the initial session timer negotiation is still ongoing. Refresher role is changed from uac to uas.
“This proxy MUST insert a Session-Expires header field into the response with the value it remembered from the forwarded request. It MUST set the value of the 'refresher' parameter to 'uac'.”
"In a session refresh request sent within a dialog with an active session timer, the Session-Expires header field SHOULD be present.“
Q: Is session timer “active”?
The UA does not include refresher in the UPDATE response. UA considers session-timer negotiation still ongoing?

## Slide 10: THE FLOW
UA Proxy AS
<-------------------
UPDATE (#5)
Supported:timer
SE:refresher=uas
<-------------------
UPDATE (#6)
Supported:timer
SE:refresher=uas
------------------->
200 (UPDATE) (#7)
------------------->
200 (UPDATE) (#8)
Require:timer
SE:refresher=uac
<-------------------
480 (INVITE) (#9)
<-------------------
480 (INVITE (#10)
When UPDATE request is sent, the initial session timer negotiation is still ongoing. Refresher role is changed from uac to uas.
“This proxy MUST insert a Session-Expires header field into the response with the value it remembered from the forwarded request. It MUST set the value of the 'refresher' parameter to 'uac'.”
"In a session refresh request sent within a dialog with an active session timer, the Session-Expires header field SHOULD be present.“
Q: Is session timer “active”?
The UA does not include refresher in the UPDATE response. UA considers session-timer negotiation still ongoing?

## Slide 11
UA Proxy AS
------------------->
INVITE (#1)
Supported:timer
SE:refresher=uac
------------------->
INVITE (#2)
Supported:timer
SE:refresher=uac
<-------------------
18x (#3)
<-------------------
18x (#4)
+++early dialog established +++
UA Proxy AS
<-------------------
UPDATE (#5)
Supported:timer
SE:refresher=uas
<-------------------
UPDATE (#6)
Supported:timer
SE:refresher=uas
------------------->
200 (UPDATE) (#7)
------------------->
200 (UPDATE) (#8)
Require:timer
SE:refresher=uac
<-------------------
480 (INVITE) (#9)
<-------------------
480 (INVITE (#10)

## Slide 12: THE BLAME
Application Server (AS) shall not change refresher role while initial session-timer negotiation is still ongoing.
User Agent (UA) shall include the refresher parameter in the UPDATE response.
Application Server (AS) shall not reject the INVITE request because of the session-timer ambiguity.
Etc etc etc.

## Slide 13: THE STANDARD
RFC 4028 does describe session-timer procedures for mid-dialog requests
  However, the procedures do not cover the case when a mid-dialog request is sent during an ongoing session-timer negotiation transaction (INVITE transaction).

## Slide 14: THE SOLUTION (DRAFT)
A Session-Expires header field can only be included in a session refresh request if there is no ongoing negotiation of usage of the session timer mechanism, and if there is no ongoing INVITE transaction.
A UA shall, if it receives a session refresh request with a Session-Expires header field during an ongoing negotiation of usage of the session timer mechanism, or when there is an ongoing INVITE transaction, send a 491 (Request Pending) response to the request.
The absence of a Session-Expires header field in a response will disable usage of the session timer mechanism only if the associated request contained a Session-Expires header field.

## Slide 15: THE COMMENTS
“I'll propose that the session timer negotiation never be done with an UPDATE within an INVITE transaction. (Regardless of whether than INVITE is negotiating a session timer or not.) I think this resolves the problem that you have encountered.” (Paul K, 09-13-2017)
  “I had a chat with some product people, and they said that there actually ARE cases where the session timer is negotiated using UPDATE when the initial INVITE transaction is still ongoing. There are cases where the INVITE only contains Supported:timer, but the actual negotiation is done using UPDATE.” (Christer H, 09-14-2017)

## Slide 16: THE COMMENTS
“I am inclined to keep things simple by saying that the 2xx response to every INVITE or UPDATE redefines the state of the session timer, either on or off. That will of course break the use case you describe above.“ (Paul K, 09-14-2017)
  “The problem here is that the UAC sends INVITE with S-E, and then receives an UPDATE with S-E before it has received a 2xx response to the INVITE - making the UAC think that there is a S-E glare situation (i.e., the UAS also tries to initiate session timer negotiation).” (Christer H, 10-05-2017)

## Slide 17: THE WAY FORWARD
Whatever solution we decide upon is going to impact existing deployments
Aim should be to minimize impact on user endpoints
  Network entities easier to fix
Aim is to fix/clarify existing session-timer mechanism, not re-define it from scratch

## Slide 18: THE END